## Choosing a Computer to Use

- This project should be harmless to do on any Windows 7 computer.

- Log onto any Windows 7 machine with an account that has Administrator privileges.

## Installing ActivePython

- We’ll use a simple Python application just to see how it uses RAM.  Python isn’t installed on Windows by default, so we’ll use ActivePython.

- Open a browser and go to activestate.com/activepython

- Click the “DOWNLOAD NOW” button to get ActivePython 2.6, as shown to the right on this page.  Save the installer file.

- Run the installer and install the software with the default options.

## Downloading the WasteMemory.py Script

- Open a browser and go to samsclass.info

- Click the “CNIT 345” link.  On the next page, click the Projects link.

- On the "Proj 5" line, point to the "WasteMemory.Python Script" link, as shown below on this page.  Right-click and save the file on your desktop.

- The file you downloaded was a Zip archive.  To extract it, on your desktop, right-click WasteMemory and click "Extract All…".  In the "Extract Compressed (Zipped) Folders" box, click Extract.

- A window appears with the WasteMemory.py file in it.  Double-click the WasteMemory.py file.

- A box pops up asking "How many MB should I waste (0 to quit):", as shown to the right on this page.

## Viewing Memory Usage with Task Manager

- On your keyboard, press Shift+Ctrl+Esc.

- Task Manager opens.  Click the Applications tab.  You should .see a Task named C:\Python26\python.exe as shown to the right on this page.

- Right-click the C:\Python26\python.exe task and click "Go To Process".

- Task manager switches to the Processes pane, and highlights the python.exe process, as shown to the right on this page.

- Notice the "Memory (Priv…" column—this shows the amount of memory each process is using now.  The Python process should be using approximately 3,000 K of RAM now, which means 3 MB.

## Using More RAM

- Find the Python window showing the "How many MB should I waste (0 to quit):" message.  Click in that window.  Type 50 and then press the Enter key.

- The Memory usage of the python.exe process should increase to approximately 52,000 K, as shown to the right on this page.

## Saving a Screen Image

- Make sure the python.exe process is visible, using approximately 52,000 K of Memory.

- Press PrintScrn to copy the whole desktop to the clipboard.

- Click Start and type in PAINT.  Click Paint.  In the untitled - Paint window, click Edit, Paste.  The image appears in the Paint window.

- In the untitled - Paint window, click File, Save.  Save the document with the filename Your Name Proj 5a, using a File Type of PNG or JPG.

## Using Task Manager's Performance Tab

- In Task Manager, click the Performance tab.  Find the Available Memory and write it down in the box below on this page.

- Find the Python window showing the "How many MB should I waste (0 to quit):" message.  Click in that window.  Type 1 and then press the Enter key.

- The Available memory shown in Task Manager should increase by approximately 50 MB immediately.

## Turning in your Project

- Email the JPEG image to me as an attachment to an e-mail message.  Send the message to: cnit.345@gmail.com with a subject line of Proj 5 From Your Name, replacing Your Name with your own first and last name.  Send a Cc to yourself.

Last revised  9-11-09

# Text boxes

Available RAM

with 50 MB Wasted: _______________