## Slide 1: CompTIA Network +
Chapter 7
Introducing Wide-Area Networks

## Slide 2: Objectives
What are three categories of wide-area networks (WAN) connections?
How are data rates measured a various WAN technologies?
Which are the characteristics of the following WAN technologies: dedicated leased line, digital subscriber line (DSL), cable modem, Synchronous Optical Network (SONET), satellite, Plain Old Telephone Service (POTS), Integrated Services Digital Network (ISDN), Frame Relay, Asynchronous Transfer Mode (ATM), and Multiprotocol Label Switching (MPLS)?

## Slide 3: Introducing Wide-Area Networks
In the early 1990s, computer-networking design guides invoked the Pareto Principle, which stated that 80% of your traffic stays local, while only 20% of your traffic leaves the local network. This was called the 80/20 Rule.
Today this is reversed, network traffic patterns are more closely approximated with 20/80 Rule.

## Slide 4: WAN Properties
Some WAN connections are considered to be always-on, in that the connection is always available without having to first set up the connection.
Conversely, some WAN technologies are on-demand, meaning that the connection is not established until needed.

## Slide 5: WAN Properties
WAN connection can generally be classified into one of three categories:
  Dedicated leased Line
  Circuit-switched Connection
  Packet-switched Connection

## Slide 6: WAN Connection Types

## Slide 7
WAN Connection Types
Connection brought up when needed, like a phone call (virtual circuit)

## Slide 8
WAN Connection Types
Always on
Multiple customers share bandwidth

## Slide 9: WAN Data Rates
WAN links are typically slower than LAN links; however, some WAN technologies boast a bandwidth capacity in tens of Gbps.
  Error in textbook near table 7-1 faster -> slower
Aside from measuring bandwidth in kbps, Mbps or Gbps, high-speed optical networks often use optical carrier (OC) levels to indicate bandwidth.
    OC-1 link is 51.84 Mbps

## Slide 10: WAN Data Rates
WAN Technology | Typical Available Bandwidth
Frame Relay | 56 kbps – 1.544 Mbps
T1 | 1.544 Mbps
T3 | 44.736 Mbps
E1 | 2.048 Mbps
E3 | 34.4 Mbps
ATM | 155 Mbps – 622 Mbps
SONET | 51.84 Mbps (OC-1) – 159.25 Gbps (OC-3072)

## Slide 11: WAN Media Types
Physical Media
  Unshielded twisted pair (UTP)
  Coaxial Cable
  Fiber-optic cable
  Electric power lines

## Slide 12: WAN Media Types
Wireless Media
  Cellular phone
    LTE goes up to 100 Mbps
    WIMAX is slower, and being replaced by LTE
  Satellite
  HSPA+
    Wireless broadband up to 84 <bps

## Slide 13: WAN Technologies
Dedicated Leased Line
  A dedicated leased line is typically a point-to-point connection interconnecting two sites.
  All the bandwidth on that line is available to those sites.
  WAN technologies commonly used with dedicated leased lines include digital circuit, such as T1, T3 circuits.
    A single 64-kbps channel is called a Digital Signal 0 (DS0)

## Slide 14: WAN Technologies
Carrier | Signal Level | # of T1 signals | # of Voice Channels | Speed
T1 | DS-1 | 1 | 24 | 1.544 Mbps
T1c | DS-1c | 2 | 48 | 3.152 Mbps
T2 | DS-2 | 4 | 96 | 6.312 Mbps
T3 | DS-3 | 28 | 672 | 44.736 Mbps
T4 | DS-4 | 168 | 4032 | 274.760 Mbps
T-carriers Single Levels

## Slide 15: Channel Service Unit / Data Service Unit (CSU/DSU)
CSU/DSU Terminating a Synchronous Circuit

## Slide 16: Point-to-Point Protocol
One of the common Layer 2 protocols used on dedicated leased lines is Point-to-Point Protocol (PPP).
  Capability to simultaneously transmit multiple Layer 3 protocols.
  PPP does this through the use of Control Protocols (CP).
  Each Layer 3 CP runs an instance of PPP’s Link Control Protocol (LCP).
    Multilink interface
      Bonds several physical connections to a single logical interface
      For load balancing
    Looped link detection
    Error detection
    Authentication
      PAP
      CHAP

## Slide 17: PAP
PAP Authentication

## Slide 18: CHAP
CHAP Authentication

## Slide 19: PPPoE

## Slide 20: Digital Subscriber Line
Commonplace in many residential and small business locations (SOHO), digital subscriber line (DSL) is a group of technologies that provide high-speed data transmission over existing telephone wiring.
DSL has several variants, which differ in data rate and distance limitations.
  Asymmetric DSL (ADSL)
  Symmetric DSL (SDSL)
  Very High Bit-Rate DSL (VDSL)

## Slide 21: ADSL Sample Topology

## Slide 22: Cable Modem

## Slide 23: SONET

## Slide 24: Satellite
High latency
Weather-sensitive

## Slide 25: Plain Old Telephone Service

## Slide 26: Integrated Services Digital Network
BRI: 128Kbps
PRI: 1.544 Mbps

## Slide 27: Frame Relay
Virtual circuits at layer 2
PVCs (permanent virtual circuits)
SVCs (switched virtual circuits)

## Slide 28: Asynchronous Transfer Mode
Asynchronous Transfer Mode (ATM) is a Layer 2 WAN technology that operates using the concept of PVCs and SVCs.
ATM uses fixed-length cells as its protocol data unit (PDU).
An ATM cell contains a 48-byte payload and a 5-byte header.
5-Byte Header
48-Byte Payload

## Slide 29: ATM

## Slide 30: ATM

## Slide 31: Multiprotocol Label Switching