Objectives

## Explain how routers are used to protect networks

## Describe firewall technology

## Describe intrusion detection systems

## Describe honeypots

Understanding Routers

# Routers

## Routers are like intersections; switches are like streets

### Image from Wikipedia (link Ch 13a)

# Understanding Routers

## Routers are hardware devices used on a network to send packets to different network segments

## Operate at the network layer of the OSI model

# Routing Protocols

## Routers tell one another what paths are available with Routing Protocols

## Link-state routing protocol

### Each router has complete information about every network link

### Example: Open Shortest Path First (OSPF)

## Distance-vector routing protocol

### Routers only know which direction to send packets, and how far

### Example: Routing Information Protocol (RIP)

# Routing Protocols

## Path-vector routing protocol

### Used on the Internet Backbone

### Example: Border Gateway Patrol (BGP)

# China’s BGP Hijacking

### Link Ch 13v

# Cisco Routers

## Image from cisco.com (link Ch 13b)

# Understanding Basic Hardware Routers

## Cisco routers are widely used in the networking community

## More than one million Cisco 2500 series routers are currently being used by companies around the world

## Vulnerabilities exist in Cisco as they do in any operating system

## See link Ch 13c

# Cisco Router Components

## Internetwork Operating System (IOS)

## Random access memory (RAM)

## Holds the router’s running configuration, routing tables, and buffers

## If you turn off the router, the contents stored in RAM are wiped out

## Nonvolatile RAM (NVRAM)

## Holds the router’s configuration file, but the information is not lost if the router is turned off

# Cisco Router Components

## Flash memory

## Holds the IOS the router is using

## Is rewritable memory, so you can upgrade the IOS

## Read-only memory (ROM)

## Contains a minimal version of the IOS used to boot the router if flash memory gets corrupted

# Cisco Router Components

## Interfaces

## Hardware connectivity points

## Example: an Ethernet port is an interface that connects to a LAN

## Cisco IOS is controlled from the command line

## The details are not included in this class

### Skip pages 376-378

# Standard IP Access Lists

## Can restrict IP traffic entering or leaving a router’s interface based on source IP address

## To restrict traffic from Network 3 from entering Network 1, access list looks like:

## access-list 1 deny 173.110.0.0 0.0.255.255

## access-list permit any

# Extended IP Access Lists

## Restricts IP traffic entering or leaving based on:

## Source IP address

## Destination IP address

## Protocol type

## Application port number

# Michael Lynn

## He presented a major Cisco security vulnerability at the Black Hat security conference in 2005

## He lost his job, was sued, conference materials were confiscated, etc.

## See links Ch 13 d, e, f, g

Understanding Firewalls

## Firewalls are hardware devices or software installed on a system and have two purposes

## Controlling access to all traffic that enters an internal network

## Controlling all traffic that leaves an internal network

# Hardware Firewalls

## Advantage of hardware firewalls

## Faster than software firewalls (more throughput)

## Disadvantages of hardware firewalls

## You are limited by the firewall’s hardware

### Number of interfaces, etc.

## Usually filter incoming traffic only (link Ch 13i)

# Software Firewalls

## Advantages of software firewalls

## Customizable: can interact with the user to provide more protection

## You can easily add NICs to the server running the firewall software

# Software Firewalls

## Disadvantages of software firewalls

## You might have to worry about configuration problems

## They rely on the OS on which they are running

# Firewall Technologies

## Network address translation (NAT)

## Access lists

## Packet filtering

## Stateful packet inspection (SPI)

## Application layer inspection

# Network Address Translation (NAT)

## Internal private IP addresses are mapped to public external IP addresses

## Hides the internal infrastructure

## Port Address Translation (PAT)

## This allows thousands of internal IP addresses to be mapped to one external IP address

## Each connection from the private network is mapped to a different public port

# Access Lists

## A series of rules to control traffic

## Criteria

## Source IP address

## Destination IP address

## Ports or services

# Packet Filtering

## Packet filters screen traffic based on information in the header, such as

### Protocol type

### IP address

### TCP/UDP Port

### More possibilities

# Stateful Packet Inspection (SPI)

## Stateful packet filters examine the current state of the network

## If you have sent a request to a server, packets from that server may be allowed in

## Packets from the same server might be blocked if no request was sent first

# State Table

## Stateful firewalls maintain a state table showing the current connections

# ACK Port scan

## Used to get information about a firewall

## Stateful firewalls track connection and block unsolicited ACK packets

## Stateless firewalls only block incoming SYN packets, so you get a RST response

## We covered this in chapter 5

# Stateful Packet Inspection (SPI)

## Stateful packet filters recognize types of anomalies that most routers ignore

## Stateless packet filters handle each packet on an individual basis

## This makes them less effective against some attacks

# Application Layer Inspection

## Stateful packet filters recognize types of anomalies that most routers ignore

## Stateless packet filters handle each packet on an individual basis

## This makes them less effective against some attacks, such as the "reverse shell"

## Application-layer firewall can detect Telnet or SSH traffic masquerading as HTTP traffic on port 80

# Implementing a Firewall

## Using only one firewall between a company’s internal network and the Internet is dangerous

## It leaves the company open to attack if a hacker compromises the firewall

## Use a demilitarized zone instead

# Demilitarized Zone (DMZ)

## DMZ is a small network containing resources available to Internet users

## Helps maintain security on the company’s internal network

## Sits between the Internet and the internal network

## It is sometimes referred to as a “perimeter network”

# Understanding the Cisco ASA (Adaptive Security Appliance) Firewall

## Replaced the Cisco PIX firewall

## One of the most popular firewalls on the market

# Configuration of the ASA Firewall

## Working with a PIX firewall is similar to working with any other Cisco router

## Login prompt

### If you are not authorized to be in this XYZ Hawaii network device,

### log out immediately!

### Username: admin

### Password: ********

## This banner serves a legal purpose

## A banner that says “welcome” may prevent prosecution of hackers who enter

# Access List

## ciscoasa( config)# show run access- list

## access- list PERMITTED_ TRAFFIC remark VPN- CONC1 TO TERMINAL CLOSET1B

## access- list PERMITTED_ TRAFFIC extended permit ip host 10.13.61.98 host 10.13.61.18

## access- list NONE extended deny ip any any log access- list CAP- ACL extended permit ip any any

# ASA Features

## Can group objects, such as terminals and serves, and filter traffic to and from them

## High throughput, and many more features

## See link Ch 13w

# Using Configuration and Risk Analysis Tools for Firewalls and Routers

## Center for Internet Security

## Cisecurity.org

## Configuration benchmarks and risk assessment tools

## Free "Router Audit Tool" and many other tools

## Link Ch13x

# Red Seal

## Commercial tool to assess network security and compiance

## Diagram shows traffic flow between devices

## Link Ch 13y

Understanding Intrusion Detection and Prevention Systems

# Intrusion Detection Systems (IDSs)

## Monitor network devices so that security administrators can identify attacks in progress and stop them

## An IDS looks at the traffic and compares it with known exploits

## Similar to virus software using a signature file to identify viruses

## Types

## Network-based IDSs

## Host-based IDSs

# Network-Based and Host-Based IDSs

## Network-based IDSs

## Monitor activity on network segments

## They sniff traffic and alert a security administrator when something suspicious occurs

### See link Ch 13o

# Network-Based and Host-Based IDSs

## Host-based IDSs

## The software is installed on the server you’re attempting to protect, like antivirus software

## Used to protect a critical network server or database server

# Passive and Active IDSs

## IDSs are categorized by how they react when they detect suspicious behavior

## Passive systems

### Send out an alert and log the activity

### Don't try to stop it

## Active systems

### Log events and send out alerts

### Can also interoperate with routers and firewalls to block the activity automatically

# Intrusion Detection and Prevention Systems

Aurora Attack--December 2009 (not in textbook)

# "Aurora" Attack on Google

## In December, 2009, Google discovered that confidential materials were being sent out of their network to China

## Google hacked into the Chinese server and stole data back, discovering that dozens of other companies had also been exploited, including Adobe and Intel

# Aurora Attack Sequence

## Attacks were customized for each target based on vulnerable software and antivirus protection

## A user is tricked into visiting a malicious website

## Browser exploited to load malware on target PC

## Malware calls home to a control server

## Local privilege escalation

# Aurora Attack Sequence

## Active Directory password database stolen and cracked

## Cracked credentials used to gain VPN Access

## Valuable data is sent to China

# New Recommendations

### Links Ch 13z1, 13z2

Understanding Honeypots

# Understanding Honeypots

## Honeypot

## Computer placed on the perimeter of a network

## Contains information intended to lure and then trap hackers

## Computer is configured to have vulnerabilities

## Goal

## Keep hackers connected long enough so they can be traced back

# How They Work

## A honeypot appears to have important data or sensitive information stored on it

## Could store fake financial data that tempts hackers to attempt browsing through the data

## Hackers will spend time attacking the honeypot

## And stop looking for real vulnerabilities in the company’s network

## Honeypots also enable security professionals to collect data on attackers

# Commercial Honeypots

# Open-Source Honeypots

# How They Work (continued)

## Virtual honeypots

## Honeypots created using software solutions instead of hardware devices

## Example: Honeyd

# Project Honey Pot

## Web masters install software on their websites

## When spammers harvest email addresses from sites, HoneyNet's servers record the IP of the harvester

## Can help prosecute the spammers and block the spam

### Link Ch 13p

## Uses a Capture Server and one or more Capture Clients

## The clients run in virtual machines

## Clients connect to suspect Web servers

## If the client detects an infection, it alerts the Capture Server and restores itself to a clean state

## The server gathers data about malicious websites

### See link Ch 13q

Web Application Firewalls (not in textbook)

# Web Application Attacks

## Normal firewall must allow Web traffic

## Doesn’t stop attacks like SQL Injection

## Figure from Imperva, link Ch 13u

# Web Application Firewalls

## There are many WAFs available

## See link Ch 13t

# How a WAF Works

## Constantly-updated list of attack signatures

## Protects a vulnerable application

Last modified 11-17-10